Comments and question by Curt Haselton on 4/14/04.

Replies by Keith Porter 6/15/04. Turn “track changes” on to see them.

This memo proposes database tables to document the results of the structural analyses as input to the damage and loss analysis. They are:

V:	Lists facility variants to be analyzed. We assume in this project that the UC Merced building (and possibly others) will be analyzed under two or more sets of assumptions, e.g., change in column reinforcement at every X versus Y stories. A variant is a version of a facility design under one of these sets of assumptions. Also use different variants to different analytical representations of the same structural system, e.g., fiber model, point hinge model, etc., to model same building, same reinforcing schedule, etc.

S:	Lists structural model simulation control parameters. Allows structures to be modeled with several realizations, such as stochastically, at Hermite-Gauss points, etc., allowing for uncertain hysteretic parameters, damping, and mass.

E:	Lists scaled ground motions and the structural model with which each is ground motion is paired.

Z:	Presents the EDP values from the structural analyses.

The tables are specified in specification tables 1-4, below. Each specification table has four columns: field name, field type, summary of field content, and comments. The specification tables use terminology of Microsoft Access.

Table 1. Variant identification table V. Table includes one record for each variant analyzed.

| Field | Type | Contents | Comments |
| --- | --- | --- | --- |
| VID | Integer | Variant ID | No blank lines, no repeats. Table contains one record for each different design and each different structural idealization of a design. |
| Var | A50 | Name or description of variant | e.g., “UCM library zone 4 col reinf sched 1, fiber model” |
| T1 | Single | Small-amplitude 1st-mode period | Sec, estimated |
| b | Single | Mean damping ratio | fraction, not percent |

At this time, we plan to do one variant and treat the design variables just like modeling variables.  If it becomes apparent that the first order approximation isn’t appropriate for the design variables, then we may need to break up the models into different variants.  Therefore, this table will likely only have one entry, but let’s keep it in the case that different design variants are needed.

Table 2.  Simulation control table S, listing parameters of structural model simulation. Table includes one record for each uncertain variable, each simulation of each variant.

| Field | Typei | Contents | Comments |
| --- | --- | --- | --- |
| SID | Autonumber | Table index; structural model simulation ID | No blank lines, no repeats. |
| VID | Integer | Variant ID | Corresponds to V.VID |
| S | Integer | Simulation within VID | e.g., if there are 10 simulations of “UCM library zone 4 col reinf sched 1, fiber model,” use 1, 2, … 10 here |
| Variable | A10 | Name of variable in question | E.g., “SCWB,” “BMD,” … “SFT.” Include only records that are relevant to this VID. |
| Definition | A255 | Define the variable in question | Please be very clear what the variable means. |
| Units | A10 | Units in which the variable is measured | e.g., “unitless,” “%,” etc. |
| Value | Single | Value of the variable |  |

Table 3.  Table E showing scaled ground motions and the structural model to which each is paired. Table contains one record for each structural analysis.

| Field | Typei | Contents | Comments |
| --- | --- | --- | --- |
| EID | Autonumber | Event ID; table index | No blank lines, no repeats. |
| RID | Integer | ID for the earthquake record | Unique identifier of unscaled recording |
| RecX | A50 | Name for the X-direction record | e.g., “CSMIP 24386 ch 16 Northridge earthquake” |
| RecY | A50 | Ditto, Y direction | Blank if 2-D analysis of a frame |
| VID | Integer | Variant ID | Corresponds to V.VID |
| S | Integer | Structural model simulation ID | Corresponds to S.S |
| T1 | Single | Period to used to scale accelerogram | sec, same as V.T1 |
| b | Single | Damping ratio used to scale accelgm | Fraction, not percent, = V.b |
| Scale | Single | Amplitude scale factor: a(t)/a0(t) | a(t) is the scaled acceleration applied to the building; a0(t) is the amplitude of the original unscaled motion. |
| Sa | Single | Spectral acceleration (at T1, b) to which the ground motion pair is scaled, in units of g | Ground motions occur in x,y pairs. The pair is scaled so that the Sa corresponds to the max direction e.g., 0.10 = 0.10g max Sa |
| SAID | Integer | Unique ID of specified Sa value | Ignore when not performing stripe analyses. |

Table 4.  Layout of structural response table Z. Table contains one record for each structural analysis and each EDP of interest.

| Field | Typei | Contents | Comments |
| --- | --- | --- | --- |
| ZID | Autonumber | Table index | No blank lines, no repeats. |
| VID | Integer | Variant ID | Corresponds to V.VID |
| SID | A2 | Struct model sim ID | Corresponds to S.SID |
| EID | Integer | Event ID | Corresponds to E.EID |
| SAID | A2 | Unique ID of Sa value | Corresponds to E.SAID |
| Sa | Single | Sa(T1, b) | Corresponds to E.Sa |
| EDPname | A7 | Name of EDP | “Collapse” = global collapse “PADIm” = (–y)/(u–y), element m, where y = yield curvature u = ult. curvature  = curvature assuming plastic hinge length d “PDAn” = peak diaphragm acceleration, floor n, max horiz. dir. “PTDna” = peak transient drift ratio floor n column line a “VRm” = shear force in element m at locn of max PADI, normalized by Vu at M = P = 0 |
| EDPID | Integer | Response param ID | 1-1 relationship between EDPname and EDPID |
| Z | Single | Value of EDP | If collapse = true, Z = 1, else, Z = 0 (or omit a record for collapse). Units: Collapse, PTD, PADI, and VR are unitless; PDA: g |

# Comments

Unclear. Please define.

Unnecessary complication. Please use a different variant ID for different analytical representations of the same structural system.

# Endnotes

Autonumber: a 4-byte integer in [–2,147,483,648, 2,147,483,647] automatically provided and incremented by Access

Integer: 2-byte integer in [–32,768, 32,767]

Single: 4-byte floating point number, 7 decimal places, in [–3.402823E38 to –1.401298E–45], [1.401298E–45 to 3.402823E38]

An: text of length n

Autonumber: a 4-byte integer in [–2,147,483,648, 2,147,483,647] automatically provided and incremented by Access

Integer: 2-byte integer in [–32,768, 32,767]

Single: 4-byte floating point number, 7 decimal places, in [–3.402823E38 to –1.401298E–45], [1.401298E–45 to 3.402823E38]

An: text of length n